# OS-Servo-Decoders Manual
Supports: OS-Servo-Decoder

## 📘 Introduction
The OS-Servo-Decoder is a simple and robust DCC accessory decoder designed for driving servo-based point motors. It supports modern model railroads with flexible configuration options, built-in frog polarity switching (optional), and direct control using both DCC accessory commands and locomotive functions (F1–F16).
Models:
- OS-Servo-Decoder-6-frog-relay — with 6 integrated frog relays
- OS-Servo-Decoder-8 — standard 8-servo model with 4-button interface
- OS-Servo-Decoder-12 — expanded version with 12 servo outputs
All variants use the same operation, configuration logic and wiring principles.

## 📚 Table of Contents
1. 📘 Introduction
2. 🔧 Features
3. 🔌 Connecting the Decoder
4. 💪 Operating the Servo Outputs
5. 🔀 Button Functions
6. 🛠️ DCC Configuration Mode
  1. 🔦 Run vs Config Mode
  2. 🌟 Storing Servo Positions
  3. 🚗 Loco Function Mode
  4. ⚖️ Address Offset
  5. ⏰ Auto-Toggle with Throttle Speed
7. 📊 Summary

## 🔧 Features
- Controls up to 6, 8, or 12 servos depending on variant
- Uses pluggable screw terminals for easy wiring
- Built-in frog relay control on 6-channel model
- Fully supports:
  - Standard turnout movement
  - Polarity switching (where supported)
  - Adjustable servo end positions (via buttons)
- Standalone configuration: no PC, CVs or programmers required
- Optional DCC locomotive function control (F1–F16)
- Supports Roco 4-address offset
- Configurable auto-toggling mode with speed control
- Easy pushbutton interface: select, toggle, fine-adjust

## 🔌 Connecting the Decoder
The OS-Servo-Decoders use the same wiring layout as the OS-Solenoid-Decoder:
- Top header: Connect either DCC track voltage or a DC power supply (max 19V)
- ⚠️ Important: Do not use AC voltage
- Servo headers: Connect each servo motor to the 3-pin connector
  - Standard layout: GND — +5V — Signal
- On the 6-relay model:
  - Screw terminals for frog connections
  - Rail power input for switching frog polarity

## 💪 Operating the Servo Outputs
Each decoder includes four buttons:
- UP and DOWN: Adjust the current position of the selected motor
- TOGGLE (short press): Toggle motor between its two stored positions
- TOGGLE (long press): Invert the frog relay direction (6-channel variant only)
- SELECT (short press): Select the next servo
- SELECT (long press): Assign a new DCC accessory address to selected motor

## 🛠️ DCC Configuration Mode
The decoder supports an advanced DCC configuration mode that works entirely from your throttle.
### 🔦 Run vs Config Mode
When powered, the decoder is normally in Run Mode. To enter Config Mode, send a DCC accessory command from locomotive address 9999, with the following:
- Speed = 0
- F0, F1, F2 = OFF
This only works if the motor was last moved via DCC loco control. In config mode, you can send function keys to change behavior.

### 🌟 Storing Servo Positions
While in Run Mode, use these functions to program:
- F1 = ON ➔ Save current position as CURVED
- F2 = ON ➔ Save current position as STRAIGHT
- F3 = ON ➔ Invert frog relay (6-relay model only)
- F0 = OFF ➔ Exit Run Mode

### 🚗 Loco Function Modes
In Config Mode, you can choose to control the decoder using loco function keys instead of accessory commands.
- F4 = ON ➔ Disable loco control (default)
- F5 = ON ➔ Enable loco function mode (F1–F16) — uses 1 address
- F6 = ON ➔ Enable 4-function mode (F1–F4) — uses 2 addresses
This allows ultra-fast switching using throttles like Roco Lokmaus or Multimaus.

### ⚖️ Address Offset
To compensate for Roco’s offset of 4, use:
F7 = ON ➔ Enable 4-address offset

### ⏰ Auto-Toggle Mode
Enable auto-toggling of a selected motor:
- F8 = ON ➔ Motor toggles every 5 seconds
  - Speed is controlled by throttle
  - Throttle direction does not matter
  - Throttle 0 = slow, Max = fast
In this mode, the motor is no longer slaved to throttle function keys.

## 📊 Summary
- Use the buttons for direct setup and servo adjustment
- Use DCC loco address 9999 with F0, F1, F2 OFF to enter config mode
- Use F1/F2 to store servo positions
- Use F4–F8 to enable loco function control, address offset or toggle modes
All OS-Servo-Decoders share this interface and logic. No computer needed. No CVs. Just wire it, address it, and run it.